## Slide 1
  2. GIS database
  3. Sentinel-2 screening
GIS DATA AND DIGITAL TOOLS FOR SURFACE WATER POLLUTION MANAGMENT
PELIN Bogdan, Moldova State University, Chisinau, Republic of Moldova
Acknowledgments: The author acknowledge the support of ZIUZEA SRL and the use of its GIS-based digital monitoring tools and platform for data visualization and surface-water quality assessment. (https://ziuzea.com/en/knowledge-hub/installations)
BACKGROUND
Surface-water monitoring often relies on fragmented spatial, field and laboratory datasets. Integrating these sources within GIS can improve spatial interpretation, temporal analysis and identification of pollution-sensitive areas.
1.
AIM OF THE STUDY
To integrate GIS, Sentinel-2 optical indicators and in-situ water-quality measurements into a digital framework for spatial assessment, monitoring and management of surface-water pollution.
2.
STUDY AREA
3.
MATERIALS AND METHODS
  Water-quality measurements
  Side observation
  Photographs
4.
Regional monitoring map (R. Moldova)
Bic river corridor - central Moldova
  Field monitoing
  Digital site profiles
  Web-based platform
  Spatial vizualization
  NDCI
  NDWI
  FAI
  NDTI
  MNDWI
  R/G
  Pollution Assessment
  Monitoing prioritisation
  Managment support
  4. Integrated analysis
*Satellite indices provide optical screening signals and do not replace field or laboratory measurements.
  5. CASE STUDY 1 - GHIDIGHICI RESERVOIR
  6. CASE STUDY 2 - STRASENI DOWNSTREAM
  7. CONCLUSION
GIS integration identified two contrasting pressure patterns: episodic phytoplankton-related change at Ghidighici Reservoir and persistent nutrient/organic pressure at Strășeni downstream. Combining Sentinel-2 screening with in-situ monitoring improves pollution interpretation, supports targeted field verification, and helps prioritize source-oriented management actions.
The main pressure is chlorophyll-related rather than turbidity-driven. The high NDCI anomaly suggests enhanced phytoplankton activity, while no comparable surface-bloom signal is evident. Field validation of chlorophyll-a and nutrients is recommended.
Persistent nutrient pressure is evident from elevated NH4-N, NO2-N and total phosphorus, accompanied by moderate organic loading. High DO indicates that oxygen depletion is not currently dominant. The nitrogen pattern suggests recent inputs or incomplete nitrification, supporting upstream source tracking and repeated monitoring.
E-mail: pelin.bogdan@usm.md