## Slide 1
MOLDOVA STATE UNIVERSITY
FENTON OXIDATION OF RESORCINOL IN AQUEOUS SOLUTION. EFFECT OF INITIAL SUBSTRATE CONCENTRATION
Larisa MOCANU (ORCID: 0000-0003-3306-5292) Maria GONȚA (ORCID: 0000-0003-3476-0967)
Laboratory of Physical and Quantum Chemistry, Institute of Chemistry, Moldova State University, Chisinau, Republic of Moldova | larisamocanu@usm.md
Aim of the Study
Why is resorcinol (RS) studied in the Republic of Moldova?
Potential endocrine disruptor
Toxic to the cardiovascular/ nervous system
Persistent
Must meet discharge limits →
0.1 mg/L
NTPA-001: discharge into natural receivers
30 mg/L
NTPA-002: discharge into sewer networks
Aim: to evaluate the effect of [RS]0 on its Fenton degradation and to find the optimal substrate concentration.
Materials and Methods
Stage 1: Fenton oxidation (batch, 60 min, 22 °C)
Fe2+ + H2O2 → Fe3+ + •OH + OH−
[RS]0 = (2.27–9.08)·10−4 M
pH = 2.5
[Fe2+]0 = 1·10−5 M
[H2O2]0 = 1·10−3 M
Stage 2: adsorption on activated carbon
Analysis: RS by UV/Vis at λ = 275 nm (T80+; R2 = 0.9995); COD at λ = 600 nm (R2 = 0.9998)
Kinetics: pseudo-first-order model; k (s−1) and t1/2 (s) from ln(C0/Ct) vs. t
Results
RS concentration decreased over time at all [RS]0, confirming effective Fenton degradation. The highest degradation efficiency was achieved at the lowest [RS]0 :
57.6%
Stage 1:
Fenton oxidation, 60 min
91.2%
Stage 2:
activated carbon adsorption
82–91%
COD reduction at all tested [RS]0
[RS]0 increased to 9.08·10−4 M → degradation (%) decreased, while the absolute mass of RS removed increased
Optimal substrate concentration: [RS]0 = 2.27·10−4 M
Fig. 1. Kinetic plots ln(C0/Ct) vs. time for RS degradation by Fenton and Fenton/UV (254 nm and 365 nm) processes.
Conclusions
The initial substrate concentration significantly influences both degradation and mineralization efficiency.
The lowest tested concentration gave the highest degradation rate under fixed Fenton reagent conditions.
Fenton oxidation can be applied to resorcinol-containing wastewaters; an optimized [RS]0 enhances removal and mineralization.
Acknowledgments
This study was supported by the research project No. 010603, Advanced research in computational and ecological chemistry, identification of technological procedures for treatment, formation of water quality and quantity, funded by NARD.
Keywords: phenol, wastewaters, Fenton processes, advanced oxidation processes
Faculty of Chemistry and Chemical Technology